## Slide 1: Speckle Interferometry: BRINGING REAL SCIENCE RESEARCH TO MASSES of STUDENTS USING SMALL TELESCOPES
Mark harris WITH SPECIAL Acknowledgments: russ genet, DAVE ROWE, pat boyce, RACHEL FREED
June 4, 2023, AAS 242, Albuquerque, NM

## Slide 2: SPECKLE INTERFEROMETRY – ELIMINATING ATMOSPHERIC TURBULANCE FOR ACCURATE ASTROMETRY
5ms Speckle image of 53 Aqr AB with Sloan Red filter
Final diffraction-limited image of 53 Aqr AB
Poor Seeing on Mt Fuji
(Courtesy Ceres MountainQuest!)
This technique uses Fourier analysis for image re-construction to eliminate atmospheric turbulence
Modern low-cost CMOS Cameras can take thousands of short exposure ~10-40 ms images
Use Open-Source Software like NINA can auto-run these masses of Speckle images
Use Speckle ToolBox (by Dave Rowe) or similar Apps to perform bi-spectrum speckle interferometry
on batches of Speckle images
Only equipment needed is small telescope, mount, red filter, barlow and low-cost CMOS camera
(Courtesy Richard Harshaw)

## Slide 3
WDS 04215-2544 0.5 ARCSECOND RECONSTRUCTED IMAGE

## Slide 4: BINARY STAR ASTROMETRY - SMALL TELESCOPE OPPORTUNITY 1
Courtesy: HNSKY Planetarium & NASA
~80% of Stars are Binary Star Systems
Of 155,541 systems listed in Washington Double Star Catalog,
only 36,653 are classified as true binary systems, 111,551 are unknown
(Courtesy WDS)
~14M Binary Star Candidates at Magnitude 14 or brighter

## Slide 5: BINARY STAR ASTROMETRY - SMALL TELESCOPE OPPORTUNITY 2
Opportunity to multiply current
WDS binaries using accurate Speckle
Interferometry
- by 10X with up to 14” Scopes
- by 90X with up to 1M Scopes

## Slide 6: Wds 11151-3929 1.45 ARCSECOND RECONSTRUCTED IMAGE