## Slide 1: Flux-Calibrating Your Spectra
Concept, Practice, and Discussion
for AAVSO Spectroscopy On-Line Meeting
Bob Buchheim
Lost Gold Observatory, AAVSO, SAS
Reference: David Boyd (2020):
A method of calibrating spectra in absolute flux using V magnitudes
https://britastro.org/wp-content/uploads/2021/05/absfluxcalibration.pdf

## Slide 2: One way of looking at the relationship between spectrum and photometry
Brighter
Fainter
Identical spectral profiles
IF/IB = 0.45
Δmag = 0.87

## Slide 3: Why flux-calibrate?
Spectral profile:
Rel Intensity vs λ
Different view of changes
Combine Spectra + Photometry
Flux-Calibrated Spectra
erg/s/cm2/Å vs λ

## Slide 4: “Flux”: What do the units mean?
Power output
(luminosity)
erg/sec
distance
cm
Flux density power/area
erg/sec/cm2
Spectral filter Δλ = 1 Å
erg/sec/cm2/Å
Atmosphere Τ(λ, α)
Observer
(exo-atmospheric)
λ, Å
Spectral flux density:
erg/sec/cm2/Å
?
?
Apparent magnitude in filter / band
There is a relationship between brightness (photometry) and spectral flux density (Y-axis of spectrum profile).
Our goal is to find it, and apply it to your “relative Intensity” spectra profiles.

## Slide 5: Simple: ISIS Command
Process spectrum as usual, FITS profile of Rel Int vs λ
  Saved into “working directory”
Then:
ISIS > Tools
> Spectra3 menu
Enter:
  Rel Int profile file name
  File name for flux-cal’d file
  V-mag
  Select “Bessel V” and “GO”
Writes flux-calibrated FITS profile to Working Directory

## Slide 6: Assumptions hidden within ISIS tool
Low- or medium-resolution spectrograph (e.g. ALPY, LISA)
  R≈ 500 – 2000
  Spectral range spans ≈ 4700 - 6700Å
“Simultaneous” V-mag of target
Your spectrum profile has been corrected for:
  Instrumental + atmospheric response
  Rel Int (exo-atmospheric) vs wavelength
  Normalized (IREL = 1) at some wavelength range
Relative Intensity
Wavelength (Angstroms)
Star spectrum profile
V-band response profile

## Slide 7: V-band flux from target:
Multiply: received flux F(λ) times V-band Response function
Integrate over all λ
= FV, in erg/s/cm2
Target spectrum (erg/s/cm2/Å)
V-response
(normalized)
FV= area under curve
Assume:
TgtFlux(λ) = K* TgtRelInt(λ)

## Slide 8: The Math …
Relative Intensity Tgt Spectrum
Flux-Calibrated Comp Star Spectrum
(e.g. CALSPEC Vega, Vmag= 0.03)
Use ISIS “Arithmetic” and “FWHM” tools to solve for value of K

## Slide 9: Flux-calibrated “Comp star” spectra: CalSpec
“Intensity” is in erg/s/cm2/Å

## Slide 10: Assumptions hidden within ISIS tool
Low- or medium-resolution spectrograph (e.g. ALPY, LISA)
  R≈ 500 – 2000
  Spectral range spans ≈ 4700 - 6700Å
“Simultaneous” V-mag of target
Your spectrum profile has been corrected for:
  Instrumental + atmospheric response
  Rel Int (exo-atmospheric) vs wavelength
  Normalized (IREL = 1) at some wavelength range
Relative Intensity
Wavelength (Angstroms)
Star spectrum profile
V-band response profile
What if the Assumptions aren’t valid for your observations?

## Slide 11
The concept & equations are valid even if:
Your spectra doesn’t span full wavelength range of V-band (e.g. my UVEX), or
You do photometry in tri-color R-G-B, or …?
The equation for K still works (using “your” filter/band and magnitude)!
HD038545
V-band Response
B-band Response
UVEX spectrum range (grating angle = 4600Å)

## Slide 12: Summary
Why flux-calibrated spectra?
Relationship between Magnitude, Flux, and Spectrum Profile
ISIS built-in Calculator
Some Equations …
Why V-magnitudes?
  Purely matter of convenience, and generally good match to Shelyak spectrographs (ALPY, LISA)
  Same concept/math works with B-band (e.g. my UVEX), or R-G-B tri-color
Questions? Discussion?

## Slide 13: Addendum: David Boyd’s equation and mine are actually identical … he uses the “Zero Point” concept (more astronomical than my equation).
David defines:
So that
My equation is:
where
Exercise for the student: show that
See next slide …

## Slide 14: Hints:
Put in the definition of ZP:
Use 10[a+b] = 10a * 10b
Use 10[logF] = F
Put in the definition of F
Then use the definition of R to show that David’s (A/R) equals my (K). Q.E.D.